## Slide 1
Forecasting Wave Runup & Overtopping
Tony Mignone National Weather Service Caribou Maine anthony.mignone@noaa.gov

## Slide 2
Service Assessment
Hurricane/Post-Tropical Cyclone Sandy
October 22-29, 2012
Finding 16:
    NWS lacks sufficient forecast guidance on inundation associated with wave runup and coastal rivers making it difficult to forecast impacts from coastal storms.

## Slide 3
Introduce Tools to forecast Wave runup and overtopping
  Runup on Sandy Beaches
  Dune Erosion
  Overtopping of Seawalls
  Overtopping of Stone Armored Revetments

## Slide 4
Runup on a Sandy Beach

## Slide 6
Parameterization for Runup Elevation
Dr. Hilary Stockdon
Ground truthed extensively
Tested in Hurricanes Bonnie, Floyd, Ike, and Ivan
Real time forecasts done every season since Hurricane Ivan

## Slide 7
Input Parameters
Foreshore Beach Slope
Deepwater Wave Height
Wave Length

## Slide 8
Computing Wave Setup
Wave Setup
Super Elevated water level due to wave action
Time averaged

## Slide 9
Wave Setup + Wave Runup
Wave Setup
Swash
Time varying water level
Large waves making incursions up the beach

## Slide 10
Infra-Gravity Waves
Infra-Gravity Waves
Long period waves of 3 to 30 minutes
Generated in areas of differential Radiation stress in swell groups in transit from the fetch area to the coast.

## Slide 11
Dune Erosion

## Slide 12
Dune Erosion
A. H. Sallenger Jr. Scaling Model “Collision Regime”
Still Water Level SWL
η
Maximum Runup level
  Above dune toe
  Below dune crest
Dune Crest
Swash
Dune
Toe
Erosion of seaward dune face

## Slide 13
Dune Erosion
A. H. Sallenger Jr. Scaling Model “Overtopping Regime”
SWL
Maximum Runup level
Infrastructure behind dune
Swash
η
  Above dune crest
Heavy
Erosion of dune
Erosion of dune

## Slide 14
Dune Erosion
A. H. Sallenger Jr. Scaling Model “Inundation Regime”
SWL
Maximum Setup Level
Infrastructure behind dune
η
Swash
Wave Setup
Wave Setup
Loss of dune

## Slide 15
Dune
Dune
Dune
Dune
Infrastructure protected by a dune

## Slide 16
Runup Matrices
Using the Stockdon Parameterization
Roque Bluffs Test Site
Matrices for April 7-8, 2016 Storm
Sallenger Regime levels are Predicted in Matrices

## Slide 17
Roque Bluffs Beach
Dune

## Slide 18
Roque Bluffs Verification Results
April 7-8, 2016 Storm
Lead Time Erosion Overwash Inundation
70 hours yes yes no
58 hours yes yes no
46 hours yes yes no
34 hours yes yes no
22 hours yes yes no
10 hours yes yes no
Occurred
Occurred
Did Not Occur

## Slide 19
Overtopping A Vertical Seawall

## Slide 20
Seawall
Time Stamp = 27th/0754 EST
Water Level = 15.476 feet
Seawall
Seawall
Stop Sign 7th &
Ocean Side Dr.
Overtopping of a Seawall
Scituate, MA January 27, 2015

## Slide 22
Overtopping Parameterization for Seawalls
Jansen and van der Meer
Off shore wave steepness
Dimensionless Freeboard for slopes
Adjusted Dimensionless Freeboard for slopes (Bruce)
Plunging wave dimensionless discharge
Mean overtopping discharge
m³/s per meter of structure length

## Slide 23
Seawall Crest
Still Water Level (SWL)
Seawall
toe
Input Parameters
Freeboard & Slope
Freeboard
Slope measured from the +2.0 MLLW level to the seawall toe
α

## Slide 24
7th Avenue Basin
Scituate Ave Basin
Seawall
Seawall
Seawall
Staff Gauge
Staff Gauge
Validation of the parameterization
Length of seawall used for calculations
Data Logger

## Slide 25
LiDAR Elevations plotted in 1 foot intervals
GIS used to compute volume of basin from LiDAR

## Slide 26
Test Events
Deploy Data Logger prior to event
Records water level every 6 min.
Volume determined from water level

## Slide 27
Wave Height
Period
Water level
Volume of Basin can be determined every 6 minutes by comparing water going in to water going out

## Slide 30
Overtopping A Stone Armored Revetment

## Slide 31
= 0.06*
Overtopping Parameterization for Stone Armored Revetments
Jansen and van der Meer
Off shore wave steepness
Dimensionless Freeboard for slopes
Plunging wave dimensionless discharge
Mean overtopping discharge
m³/s per meter of structure length
= 0.06*

## Slide 32
α
Input Parameters
Freeboard & Slope

## Slide 33
Seawall Road LiDAR Elevations

## Slide 34
Forecast Matrices for Overtopping Discharge Volume
Seawall Road Test Site
Matrices for April 7-8, 2016 Storm

## Slide 35
Impact Index Scale
Currently predicted volume is treated as an index with correlated impacts

## Slide 36
February 8, 2016

## Slide 37
Attempt to Validate predicted volume

## Slide 38
Pond and Marsh Area Behind Sea Road
Pond behind road sometimes floods from overtopping water and can be used as collection area to validate predictions

## Slide 39
Pond and Marsh Area Behind Sea Road
Area at 11 Feet NAVD88 = 20.6 Acres
Volume at 11 Feet NAVD88 = 50,000 Cubic Meters
(From GIS)
Culvert Outlet Pipe

## Slide 41
Manning Equation
More than half full
Less than half full
h = 2r - y
θ = 2 arc cos
A = -
P = 2𝝅r – rθ
= A/P
h
h
h = y
θ = 2 arc cos
A =
P = rθ
= A/P
Q = A
Q =
S = bottom slope of channel
n = Roughness Coefficient
Used to Compute volume flowing through pipe

## Slide 42
Seawall Road Webcam
Can deploy data logger or install staff rod that can be read from webcam

## Slide 43
Wave Height
Period
Water level
Modeling Seawall Road
Flooded Pond
Will allow volume validation
Results can be compared with other sites

## Slide 44
Questions ??