## Slide 1
Jonathan J. Gourley
National Severe Storms Lab
University of Oklahoma
Norman, Oklahoma, USA
The Past, Present, and Future of Flash Flood Prediction

## Slide 2: NWS Flash Flood Guidance System
Flash Flood Guidance (FFG): average rainfall over a specified area and time duration required to initiate flooding on small streams
FFG (mm) computed for accumulation periods of 1-, 3-, 6-hr (12, 24 also used)
If rainfall exceeds FFG, then a forecaster will consider issuing a flash flood warning

## Slide 3: How is FFG derived ?
Lumped SAC-SMA model run under different rainfall scenarios to produce rainfall-runoff curves
Curves subject to change due to initial soil moisture states, evapotranspiration
Thresh runoff values (pre-computed) looked up on curves to get FFG
Saturated
soil states
ThreshR
1-hr FFG

## Slide 4: Evaluation of the Operational Tools used for Flash Flood Forecasting in the US
Jess Erlingis
Race Clark
NSF Graduate Research Fellowship
NWS Advanced Hydrologic Prediction Service

## Slide 5
R. Clark, et al. Evaluation of Flash Flood Guidance in the U.S.
FFG Production
LFFG – Lumped FFG
  Lumped-parameter basins (~300 – 3,000 km2); SAC-SMA model
GFFG – Gridded FFG
  high-res product based on NRCS Curve Number method
DFFG – Distributed FFG
  Continuous-API (Antecedent Precipitation Index)
FFPI – Flash Flood Potential Index
  Quasi-static; geographical characteristics (slope, land cover, wildfire, soil type, …)

## Slide 6
Study Period
1 Oct 2006 – 31 Aug 2010
Changes in FFG generation method occurred in late 2007 or early 2008

## Slide 7
Map of what type of FFG runs at various RFCs

## Slide 8
Map of what type of FFG runs at various RFCs

## Slide 9
HITS - Black Arrows
MISSES – Red Arrows
No FALSE ALARMS – all contiguous areas of ratio > 1.0 have at least one observation

## Slide 10: Results – NWS Storm Data Analysis

## Slide 11: Results – USGS Stage Height Analysis

## Slide 12
R. Clark, et al. Evaluation of Flash Flood Guidance in the U.S.
N = 820
N = 5,530
N = 7,670
GFFG
FFPI
LFFG
N = 710
DFFG

## Slide 13
R. Clark, et al. Evaluation of Flash Flood Guidance in the U.S.
Conclusions/Recommendations
All methods of FFG in all regions have low CSI (high false alarms; low probability of detection)
  CSI = 0.19 over Middle Atlantic RFC using 1-hr DFFG & 1.25 QPE-to-FFG ratio
  This value should be considered as the benchmark skill for future developments
Both evaluations indicate the worst performance was in CNRFC, CBRFC, NWRFC, and NERFC
NWS Storm Data has large sample sizes, so we use it for intercomparison
  DFFG is best method
  LFFG and GFFG have similar skill but GFFG has better resolution
  FFPI has lowest skill and should be used sparingly
National system w/consistent skill desirable; but include ability to include local modifications
http://www.nssl.noaa.gov/projects/flash

## Slide 14: Threshold frequency method for flash flood prediction
Take longest available gridded rainfall record
Simulate flow with hydrologic model for period of rainfall recording annual maximum flows @ each grid cell
Compute Log-Pearson III distribution from annual maximum sim flows (gives mean, standard deviation and skew parameters)
From this distribution estimate we can estimate return period for any discharge value at every grid point
Streamflow (cms)
Return Period (years)
Time
2
Q2
Inherent bias correction for inputs+model
Reed et al. (2007)

## Slide 15: Ensemble Framework For Flash Flood Forecasting (EF5) supports 2 distributed models
HL-RDHM
CREST
Concepts from SAC-SMA model
Runs operationally in US NWS
Has a priori parameters
4-km/1-hr resolution
Wang et al. (2011) Hydrol. Sci. J.
Koren et al. (2004) J. Hydrol.
Figure adapted from UC-Irvine
Concepts from Xinanjiang model
Runs operationally over globe at OU and NASA
Has a priori parameters
1-km/5-min resolution

## Slide 16: CREST – a priori parameters
1/(Manning N)
Ksat
% Impervious Area
Roughness coefficient controls quickflow routing speed
Saturated hydraulic conductivity controls slowflow routing speed

## Slide 17: 2-yr return period simulated flows from NEXRAD archive (2002-2010)
“Flash flood alley”
(floodsafety.com)
?

## Slide 18
Gourley et al. (2012) Hydro. Sci. J.

## Slide 19
A demonstration system for real-time flash flood prediction
FLASH: Flooded Locations and Simulated Hydrographs

## Slide 20: The 1D (traditional) way of doing hydrology

## Slide 22: Oklahoma City Flash Flood
0
325
Accumulation (mm)
Morning of June 14th, 2010
12” of rain in < 6 hours!
Lots of flooding & property damage, thankfully no loss of life
Photos courtesy of OKC Dept. Public Works

## Slide 23
Comparison of Q2 radar-only 24-hr rainfall to Mesonet gauges

## Slide 25: Evaluation of Flash Flood Simulations
Max Return Period (years)
1
10
SHAVE Reports
No Flooding
Flooding
Severe Flooding
US NWS Flood Report
Severe Hazards Analysis and Verification Experiment
Ortega et al., BAMS (2009)

## Slide 27
Hurricane Sandy

## Slide 29: Distributed Flood Severity Index

## Slide 30
Precip Forcing
  Q2 rainfall rate
  Q2 precip type
  TMPA-RT
  NWP forecasts
Ensemble Framework For Flash Flood Forecasting (EF5)
Evapotranspiration
  FEWS NET PET
  HRRR temp, etc
  Land surface model
Surface Runoff
  SAC (HL-RDHM like)
  VIC (CREST like)
  HyMOD
Groundwater
  MODFLOW
Routing
  Kinematic wave
  Linear reservoir
Snowmelt
  SNOW-17
  HRRR temp
State Estimation (EnKF)
  USGS streamflow
  AMSR-E soil moisture
Forecast
  Threshold frequency
  Probability of flood
  Probability of damage
Current Version
Future Addition
Param Estimation (DREAM)
  USGS streamflow
  AMSR-E soil moisture

## Slide 31: Probabilistic Flash Flood Forecasting using Ensemble Stormscale Precipitation Forecasts
Jill Hardy
Gina Hodges
NSF Graduate Research Fellowship

## Slide 32: Maximum Return Periods – OKC Flash Flood
Q2 (observed)
Best member
Ensemble mean
Probability matched mean
Promising performance from a 12-hr forecast !

## Slide 33: The use of SHAVE and NWS flash flood reports for impact characterization and prediction
Martin Calianno
Laboratoire d'étude des Transferts en
Hydrologie et Environnement, Grenoble, France

## Slide 34: Are simulations of flash flood severity related to economic impact?
From hydrologic model
From NWS StormDat reports

## Slide 35: How does FLASH differ from DHM-TF package?
Resolution: FLASH runs on back-end of NMQ/Q2 rainfall generation and provides forecasts at the flash flood scale (1 km/5 min presently, with upgrade to 250 m in March vs. 4 km/1 hr)
Probabilistic instead of deterministic
Will incorporate GIS exposure factors to yield impact-specific products
Framework readily accommodates forcing from contemporary QPFs (e.g., stormscale ensembles)
FLASH is a centerpiece for R&D

## Slide 37: Relevant Literature
Calianno, M., I. Ruin, and J. J. Gourley, 2013: Supplementing flash flood reports with impact classifications, J. Hydrol., 477, 1-16. doi:10.1016/j.jhydrol.2012.09.036
Gourley, J. J., Y. Hong, Z. L. Flamig, A. Arthur, R. A. Clark, M. Calianno, I. Ruin, T. Ortel, M. E. Wieczorek, E. Clark, P.-E. Kirstetter, and W. F. Krajewski, 2013: A unified flash flood database over the US., Bull. Amer. Meteor. Soc., (in press)
Clark, R. A., J. J. Gourley, Z. L. Flamig, Y. Hong, and E. Clark, 2013: CONUS-wide evaluation of National Weather Service flash flood guidance products, Wea. Forecasting (in review).
Gourley, J. J., J. M. Erlingis, Y. Hong, and E. Wells, 2012: Evaluation of tools used for monitoring and forecasting flash floods in the United States. Wea. Forecasting, 27, 158-173, doi: 10.1175/WAF-D-10-05043.1.
Gourley, J. J., Z. L. Flamig, Y. Hong, and K. W. Howard, 2012: On the accuracy of the past, present, and future tools for flash flood prediction in the USA. IAHS Publ. 351, ISBN 978-1-907161-26-1, 435-440.
Wang, J., Y. Hong, L. Li, J. J. Gourley, S. I. Khan, K. K. Yilmaz, R. F. Adler, F. S. Policelli, S. Habib, D. Irwin, A. S. Limaye, T. Korme, and L. Okello, 2011: The coupled routing and excess storage (CREST) distributed hydrological model. Hydrol. Sci. Journal, 56, 84-98, doi: 10.1080/02626667.2010.543087.
Gourley, J. J., J. M. Erlingis, T. M. Smith, K. L. Ortega, and Y. Hong, 2010: Remote collection and analysis of witness reports on flash floods. J. Hydrol., 394, 53-62, doi: 10.1016/j.jhydrol.2010.05.
Ortega, K.L., T.M. Smith, K.L. Manross, K.A. Scharfenberg, A. Witt, A.G. Kolodziej, and J.J. Gourley, 2009: The severe hazards analysis and verification experiment. Bull. Amer. Meteor. Soc., 90, 1519-1530.