## Slide 1: INSITE – An IDSS Tool for Aviation
Missy Petty, Geary Layne, Brian Etherton, Paul Hamer, Mike Rabellino
VLab Forum
17 February 2016

## Slide 2: Forecast Impact and Quality Assessment Section
Mission: Advance the understanding and use of weather information through impact-based assessments and targeted information delivery to benefit decision making in response to high-impact weather events
Sponsors
  NWS: NextGen Program and Aviation and Space Weather Services Branch
  FAA: Aviation Weather Research Program (QA PDT)
Activities
  Independent quality assessments
  Verification in operational context
  Technologies
Notes: Focus is measuring skill of products when it matters

## Slide 3: Collaborative Aviation Weather Statement (CAWS)

## Slide 4: INSITE
Development sponsored by NWS NextGen Program
  Aligned with NWS Weather Ready Nation initiative of Impact-based Decision Support Services

## Slide 5: Impact-based Decision Support
A weather decision service for
common situational awareness
and forecast preparation
Weather
Forecasts,
Observations
Decision Criteria
Traffic Flow Information
INSITE: INtegrated Support for Impacted air Traffic Environments
INSITE
TFM Planner
Weather Forecasts & Observations
CIWS
LAMP
CoSPA
CCFP
NWS Forecaster
Impact-based Forecast Information

## Slide 6: INSITE Features
Features support forecaster identification of convective weather potentially impactful to air traffic
Several convective forecast products, plus observations
Overlays of routes and Control Centers (ARTCCs)
Airspace constraint fields (Flow Constraint Index) derived from blend of weather and traffic data
Confidence information for forecast constraint
Displays of both raw weather and constraint fields
‘Synthesis’ product, where different forecast products are blended into a single forecast of constraint using performance information
Summary constraint information for regions of interest (default ARTCCs or user-drawn)
  Drill-down capabilities to identify potential impacts to related routes or ARTCCs
Historical playback feature to review past events

## Slide 7: INSITE – Main Page

## Slide 8: INSITE
Raw weather with core airport overlays

## Slide 9: INSITE
Raw weather graphics and route overlays indicate this line of convection could be impactful to East-West traffic
INSITE provides a metric that is a quantitative measure of how much impact is likely

## Slide 10
Blue lines: Corridor boundaries.
Red area: Area of hazardous weather.
Arrow A: Distance across corridor in absence of hazards.
Arrows B and C: Distance across the available airspace around a hazard.
Flow constraint is 1- (MincutHazard/MincutCorridor)
Apply weighting scheme (traffic density)
FCI of 1.0 corresponds to most constrained, 0.0 corresponds to none.
Can compute FCI for any type of forecast (probabilistic, deterministic)
Hazard
Corridor Axis
Corridor
MincutCorridor
MincutHazard
A
B
C
Flow Constraint Index (FCI)

## Slide 11: FCI Hexagonal Grid
Corridor

## Slide 12: FCI Example in INSITE
FCI
TRAFFIC FORECAST
AIR TRAFFIC FLOW CONSTRAINED BY WEATHER
CONVECTION FORECAST

## Slide 13: FCI Traffic Weighting – Historic Data
ASDI Data from 2014 convective season (May-Sept)
Flights corresponding to major carriers, operating at OEP 35 airports
Data representing ‘ideal scenario’ for standard routes
  Clear air days
  First flight plan
Traffic density stratified by day of week and hour of day

## Slide 14: FCI Traffic Weighting – Current Data
Ingest real time air traffic from the ASDI data set
Determine the set of most recent flight plans, planned aircraft locations
Incorporate ‘planned’ traffic density into the FCI
A FACET snapshot of air traffic over the United States on July 10, 2006, at 2:45 p.m. EST.
Image Credit: NASA Ames Research Center

## Slide 15: INSITE
Raw weather graphics and route overlays indicate this line of convection could be impactful
INSITE provides a metric that is a quantitative measure of how much impact is likely

## Slide 16: FCI in INSITE – Our Case
FCI is depicted via ‘heat map’
For this case, FCI indicates a large area of constraint as forecast by the NSSL WRF

## Slide 17: FCI in INSITE – Our Case
Users can click on the ‘up arrow’ button on to view FCI computed with current traffic
‘Current traffic’ view indicates that planned routes are still impacted by the convection depicted by the NSSL WRF

## Slide 18: FCI in INSITE – Areas of Interest
Users can draw their own polygons for more detailed interrogation of a specific region

## Slide 19: FCI – Summary Information
Bar charts on far left are time series of constraint as identified by FCI
Each bar corresponds to a polygon drawn on the geographical map

## Slide 20: Constraint and Confidence Bars (CC-Bars)
Past Valid Times
Now (Reference Time)
Future Valid Times

## Slide 21: Constraint and Confidence Bars (CC-Bars)
Polygon text: Click to rename polygon
Top bar: Forecast constraint
Bottom bar: Constraint derived from observations
Black horizontal line: Forecast confidence level between 0 and 100
Click to delete polygon
Click to navigate to constraint details for polygon
Severity Categories

## Slide 22: Constraint and Confidence bars
Constraint and Confidence (or Consistency) bars (CC bars) are provided on the left side
Confidence Information
Confidence is based on long-term historical performance of the forecast products, and also includes a prolonged forecast latency penalty

## Slide 23: Products Featured in INSITE
INSITE products:
  HRRR
  NSSL WRF
  SREF
  LAMP
  CCFP
  CIWS
Raw product or derived constraint (FCI)

## Slide 24: Synthesis Product
The synthesis is a blend of the individual FCI’ed products
  All
  High-res only
Product weights based on historical performance, inter-model consistency

## Slide 25: Synthesis
CCFP
LAMP
SREF
HRRR
NSSL WRF
Synth Hi-res
Synth All

## Slide 26: Constraint and Confidence bars
Constraint and Confidence (or Consistency) bars (CC bars) are provided on the left side
Confidence Information
Confidence is based on long-term historical performance of the forecast products, and also includes a prolonged forecast latency penalty
For synthesis product, horizontal line is grey and indicates level of consistency between constituent forecasts

## Slide 27: Further Regional Interrogation
Clicking on the ‘green arrow’ icon above the CC-bar navigates the user to more detailed information about the corresponding polygon

## Slide 28: NAS Elements Within a Polygon/Area
CC-bars correspond to high altitude routes that pass through the selected polygon area

## Slide 29: NAS Elements Within a Polygon/Area
Routes are listed by rank, with the most impacted at the top of the list, the least impacted at the bottom of the list
Impact, as used to rank the routes, is for future times only
Intersecting ARTCCs are also viewable, using the gear symbol

## Slide 30: NAS elements within a polygon/area
Hovering over one of the CC-bars highlights the route associated with that CC-bar on the FCI image

## Slide 31: NAS elements within a polygon/area
Clicking on one of the CC-bars brings up a time series of the FCI values from all products for the time period from 4 hours before to 12 hours after the reference time

## Slide 32: NAS elements within a polygon/area
Hovering over a product name causes that product’s time series to become bold (in this case, the dark blue NSSL WRF)

## Slide 33: Use Case
INSITE Operational Scenario Steps
Identify potential areas of air-traffic constraints in area of responsibility
Narrow down area of interest using polygon drawing tool
Use these areas of constraints as first guess impact areas in CAWS
Identify geographic areas with constraints above moderate severity threshold
Identify potential time of onset and cessation
Adjust forecast based upon model trends using confidence in CC bars
Adjust forecast based upon model consistency in CC bars
Compare potential areas of air-traffic constraints with other model guidance

## Slide 34
Collaborative Aviation Weather Statement 003 NWS Aviation Weather Center Kansas City MO 1450 UTC Mon 06 Jul 2015 Weather: Thunderstorms Valid: 1800-2200Z ARTCCs affected: ZFW, ZKC, ZMP Terminals affected: CCFP: 15Z - Coverage too low SUMMARY: Thunderstorms expected to develop across ZKC by 18Z and intensify into a line by 20-22Z. DISCUSSION: Current storms across N KS/SE Neb will intensify after 18Z and form a broken line by 20Z and a significant solid line by 22Z with tops FL400+. Further south across the panhandle TX and W OK a broken line should begin to form around 22Z. An additional CAWS may be needed as the storms pushes eastward.
Collaborative Aviation Weather Statement (CAWS)
CCFP
CAWS

## Slide 35: INSITE v4
Funding organization: NWS NextGen Program
INSITE 4 to be released late May 2016, available for OB/CAWS activities
  Addition of MRMS analyses
  Switch from AWC SREF product to NCEP/NCO SREF product
  Numerous UI updates (such as black background, improved product navigation, more help info)
  New “Alert” feature – system identification of areas that are in excess of a given FCI value
35

## Slide 36
Alert dashboard
When user clicks specific valid time, the alert polygons and heat map for that valid time will be displayed
INSITE Alert Feature – Mockup

## Slide 37: Transition to NWS Operations
Operational host: IDP
IOC
  INSITE v4
    Switch to all operational NWS products (replace CIWS with MRMS, NSSL-WRF with HiRes NMM/ARW runs)
  May 2017
Where in the process?
  Have begun the necessary coordination with IDP
  Initial design review
  Technical documentation
37

## Slide 38: Contacts
Feedback and questions on INSITE and its use are welcomed
NOAA/ESRL contact:
  Missy Petty melissa.a.petty@noaa.gov
NOAA/NWS contact:
  Jamie Vavra jamie.vavra@noaa.gov