## Slide 1: Focus Group Evaluation CMAQ PM2.5 and Ozone 2024
Michael Geigert
Bureau of Air Management

## Slide 2: Introduction
The summer of 2024 was the warmest over the past 6 years, with June being the hottest month.
Surface PM2.5 levels due to smoke were lower than last year, but likely raised ozone levels at the surface on several occasions.
Most of the ozone episodes were well modeled with fewer false alarms than last year.
During August, the PM2.5 BC model retained moderate levels for several days, even though good air quality was being monitored.

## Slide 3: 2024 Ozone Exceedance Summary Table
Connecticut had 23 ozone exceedance days with the highest levels occurring in June.

## Slide 4: Ozone Site Exceedances
Connecticut had more site exceedances in 2024 than the past 5 years. This surpassed 2023, when smoke was more of an issue.
Chart: CT Accumulated Site Exceedances 2024

## Slide 5: Cooling Degree Days
This was the warmest summer since 2018 for cooling degree days, which may have been a factor for the increase in site exceedances.
Chart: Accumulated Cooling Degree Days 2024 (65°F)

## Slide 6: Monthly Temperature Departures
May was well above normal for the entire Northeast, with temperatures cooling to near normal levels by August.

## Slide 7: Ozone Model Evaluation
The upcoming slides are from selected ozone episodes throughout the summer.
The images from the ‘raw’ model output are compared to that from the bias corrected.
All images are from the 06z Day 1 model run.
Time series graphs are included showing comparisons with observed data for sites of interest.

## Slide 8: June 2, 2024 Ozone
Three sites in Connecticut exceeded the 70 ppb NAAQS, surrounded by a large area of moderate ozone.

## Slide 9: June 2, 2024 Ozone Model Performance
The raw output showed USG levels, albeit displaced too far south. The BC output was much too low.
June 2, 2024 06z Ozone
June 2, 2024 06z Ozone BC

## Slide 10: June 3, 2024 Ozone
This was a widespread coastal event, extending into northwest Connecticut. A high of 81 ppb was recorded at Stratford.

## Slide 11: June 3, 2024 Ozone
A HMS smoke plume was analyzed over the East Coast, with the Redhook NY backscatter LIDAR showing a light smoke plume reaching the surface.

## Slide 12: June 3, 2024 Ozone Model Performance
On this day, both models greatly under estimated the ozone levels. Smoke?
June 3, 2024 06z Ozone
June 3, 2024 06z Ozone BC

## Slide 13: June 2-4, 2024 Ozone Model Stratford
The raw model performed the beat for this episode, but June 3rd was modeled much too low in both versions.

## Slide 14: June 4, 2024 Ozone
June 4th only had one exceedance in far western Connecticut.

## Slide 15: June 4, 2024 Ozone Model Performance
The raw model had the USG displaced too far south.
June 4, 2024 06z Ozone
June 4, 2024 06z Ozone BC

## Slide 16: June 2-4, 2024 Ozone Model Danbury
Both models missed the ozone exceedance at Danbury.

## Slide 17: June 13, 2024 Ozone
This was another widespread exceedance across the State. East Hartford was the highest at 75 ppb.

## Slide 18: June 13, 2024 Ozone Model Performance
The model totally missed the ozone exceedances on this day.
June 13, 2024 06z Ozone

## Slide 19: June 13, 2024 Ozone Model East Hartford
The East Hartford monitor had the highest 1-hour ozone.

## Slide 20: June 18, 2024 Ozone
These ozone exceedance occurred well inland, being pushed northward by the Atlantic southerlies.

## Slide 21: June 18, 2024 Ozone Model Performance
Both models captured the ozone plume very well.
June 18, 2024 06z Ozone
June 18, 2024 06z Ozone BC

## Slide 22: June 18-20, 2024 Ozone Model East Hartford
Both models did well for June 18-19, but missed the ozone spike on June 20th over East Hartford on Day 3.

## Slide 23: June 19, 2024 Ozone
The highest ozone levels once again occurred well inland.

## Slide 24: June 19, 2024 Ozone Model Performance
Both models did well for placement and concentrations.
June 19, 2024 06z Ozone
June 19, 2024 06z Ozone BC

## Slide 25: June 19-21, 2024 Ozone Model East Hartford
Day 2 over East Hartford is once again modeled much too low.

## Slide 26: June 20, 2024 Ozone
June 20th was the highest ozone day over Connecticut

## Slide 27: June 20, 2024 Ozone Model Performance
Models had good placement, but levels were too low.
June 20, 2024 06z Ozone
June 20, 2024 06z Ozone BC

## Slide 28: June 20, 2024 Ozone Model East Hartford
Ozone levels were somewhat higher than previous runs, but still too low.

## Slide 29: June 20, 2024 smoke Analysis
HMS smoke analysis confirms the presence of a smoke plume overhead. The NY Redhook backscatter LIDAR shows smoke aerosols reaching the surface.

## Slide 30: June 21, 2024 Ozone
June 21st monitored high ozone levels along the Connecticut coast. Westport had a high of 87 ppb.

## Slide 31: June 21, 2024 Ozone Model Performance
The BC version was lower than what was observed, so the raw model is preferred.
June 21, 2024 06z Ozone
June 21, 2024 06z Ozone BC

## Slide 32: June 21-22, 2024 Ozone Model Westport
The raw model performed the best for Westport day 1, but was too high for day 2.

## Slide 33: June 22, 2024 Ozone
On June 22nd, Westport had the highest ozone at 86 ppb.

## Slide 34: June 22, 2024 Ozone Model Performance
The raw model better captured the high ozone at Westport.
June 22, 2024 06z Ozone
June 22, 2024 06z Ozone BC

## Slide 35: June 22, 2024 Ozone Model Performance
The day 1 model run for Westport shows the BC version being too low.

## Slide 36: July 15, 2024 Ozone
This was the beginning of a 3-day episode. The highest ozone was 81 ppb at Stratford.

## Slide 37: July 15, 2024 Ozone Model Performance
For this case, the BC version was more accurate than the raw version.
July 15, 2024 06z Ozone
July 15, 2024 06z Ozone BC

## Slide 38: July 15-17, 2024 Ozone Model Performance
On July 15th, the Greenwich monitor had a sudden dip that confounded the models. There was a sudden spike on Day 2 that both models missed.

## Slide 39: July 16, 2024 Ozone
July 16th was a widespread event, with Westport being the highest at 85 ppb.

## Slide 40: July 16, 2024 Ozone
Smoke was again present on the HMS analysis. The early morning satellite image also showed smoke.

## Slide 41: July 16, 2024 Ozone Model Performance
The raw version best captured the widespread event and the high ozone at the Westport monitor.
July 16, 2024 06z Ozone
July 16, 2024 06z Ozone BC

## Slide 42: July 16-18, 2024 Ozone Model Performance
Both models performed in a similar fashion, but they missed the day 1 ozone spike, possibly due to smoke enhancement.

## Slide 43: July 17, 2024 Ozone
June 17th only had a few ozone exceedances around NYC. Danbury and Greenwich both monitored 73 ppb.

## Slide 44: July 17, 2024 Ozone Model Performance
The raw model was too high and the BC was too low, but did well for Greenwich.
July 17, 2024 06z Ozone
July 17, 2024 06z Ozone BC

## Slide 45: July 17-18, 2024 Ozone Model Performance
This shows the raw model being much too high for Greenwich and the BC being very close.

## Slide 46: August 25, 2024 Ozone
August 25th was a coastal event with Greenwich being the highest at 75 ppb.

## Slide 47: August 25, 2024 Ozone Model Performance
The raw version captured the event well, while BC was much too low.
August 25, 2024 06z Ozone
August 25, 2024 06z Ozone BC

## Slide 48: August 25-27, 2024 Ozone Model Performance
There was a growing spread of >10 ppb between the raw and BC at Greenwich. Both models were much too low on day 2.

## Slide 49: August 26, 2024 Ozone
Only two Connecticut monitors exceeded on August 26th, with Westport at 72 ppb.

## Slide 50: August 26, 2024 Ozone Model Performance
The raw version was most correct on this day, with the BC version much too low.
August 26, 2024 06z Ozone
August 26, 2024 06z Ozone BC

## Slide 51: August 28, 2024 Ozone
The ozone was highest on east coastal Connecticut, with Madison at 82 ppb.

## Slide 52: August 28, 2024 Ozone Model Performance
Both models vastly under estimated the ozone levels on this day.
August 28, 2024 06z Ozone
August 28, 2024 06z Ozone BC

## Slide 53: August 28, 2024 Ozone Model Performance
Both models were about 20 ppb too low for Day 2 at Madison.

## Slide 54: August 28, 2024 Smoke Analysis
Once again, there was a vast smoke plume being reported that may have enhanced the ozone levels.

## Slide 55: Ozone Over Predictions July 8, 2024
There were no exceedances on this day. The BC version correctly lowered the ozone values for Connecticut.
July 8, 2024 06z Ozone
July 8, 2024 06z Ozone BC

## Slide 56: Ozone Over Predictions
Only Cornwall exceeded on July 9th at 72 ppb. The raw version was too widespread while the BC was more accurate, but displaced to the south.
July 9, 2024 06z Ozone
July 9, 2024 06z Ozone BC

## Slide 57: Ozone Over Predictions
There were no exceedances on this day. The BC was still too high along the coast.
August 3, 2024 06z Ozone
August 3, 2024 06z Ozone BC

## Slide 58: PM2.5 Model Performance
Although there was a smoke plume overhead, the surface PM2.5 levels were modeled too high over the Northeast states.
July 31, 2024 06z PM2.5 BC
Over Prediction

## Slide 59: PM2.5 Model Performance
Moderate PM2.5 levels were monitored across New England. The PM2.5 BC model was forecasting mostly good levels.
August 14, 2024 06z PM2.5 BC
Under Prediction

## Slide 60: PM2.5 Model Performance
By August 15th, the model was showing some moderates, while every monitor was at moderate levels.
August 15, 2024 06z PM2.5 BC
Under Prediction

## Slide 61: PM2.5 Model Performance
By August 17th, the model was forecasting moderate PM2.5, just slightly below monitored levels.
August 17, 2024 06z PM2.5 BC
Good Forecast

## Slide 62: August 18th Rainfall
On August 18th, historic rainfalls occurred over parts of Connecticut, greatly reducing the PM2.5 levels

## Slide 63: PM2.5 Model Performance
On August 19th, the model was still holding on the moderate levels, while very low PM2.5 levels were being monitored.
August 19, 2024 06z PM2.5 BC
Over Prediction

## Slide 64: PM2.5 Model Performance
On August 20th, the model was still mostly moderate, while very low PM2.5 levels were being monitored.
August 20, 2024 06z PM2.5 BC
Over Prediction

## Slide 65: Conclusions
The ozone models performed much more consistently this year, with the BC version very close to the raw during a few episodes.
During other episodes the BC was bias lower by 10 ppb or more, which caused it to under predict during widespread events.
There appeared to be less false alarms than last year for ozone.
The urban plume enhancement downwind of NYC that I observed last year, did not seem to be happening this year.
There were some sudden spikes in monitored ozone, likely due to smoke enhancement that the models could not predict.
The PM2.5 BC is usually very reliable, but during mid-August it began over-predicting PM2.5 levels, possibly because of missing the rain event or from recirculation from off the domain.