## Slide 1: Minnesota Heavy Wildfire smoke events 2014-2023
Ryan Lueck
Minnesota Pollution Control Agency

## Slide 2: Motivation
Better understand past wildfire smoke events to help forecast future events by establishing a climatology/goal posts
  Silver lining to the 2021 & 2023 season
Solidify conceptual models
  Synoptic, surface, other weather patterns & parameters
  Fire weather conditions
Create another angle from which to approach the forecast, apart from models alone
  Variety of tools available for context in weather forecasting such as analogs
Help inform a potential future “outlook” for partners to increase lead time and awareness of potential smoke intrusions
Notes: *Weekly MNICS briefings – we try to provide a daily “probability of alert” through the next 7 days

## Slide 3: Overview
Identified all Minnesota monitors that had AQI of 90 or greater for PM2.5
  Focused on daily NAAQS exceedance criteria, despite the limitations (bulk of smoke not likely to fall neatly within the midnight to midnight timeframe, etc.)
  Added a 10 AQI buffer to capture some of the events that may have exceeded via a rolling 24 hour average
Filtered out all non-wildfire events by reviewing archived NOAA Hazard Mapping System smoke plume analysis and polar-orbiting satellite data
Notes: *I believe there are 25 total PM2.5 “Minnesota monitors” which includes one in Fargo, ND and La Crosse, WI
*MN centric, but hopefully of use or interesting to others

## Slide 4: Overview
Years examined: 2014 - 2023
Number of days at least one MN monitor reached an AQI of 90+: 68
Number of events: 25
  Defined as an episode of heavy smoke with hourly concentrations of 35.5 ug/m^3 at minimum somewhere in Minnesota within a +/-24 hour buffer of an AQI 90+ day, to simulate how we’d handle Air Quality Alerts (continuation vs new alert)
  Each event lasts 2.7 days on average
Notes: *Still small, but workable sample size thanks to the 2021 and 2023 wildfire seasons.
*These are the worst events. There are many more that involved 6-12 hours of alert-level concentrations but didn't average out high enough.

## Slide 5: Overview
Years examined: 2014 - 2023
Number of days at least one MN monitor reached an AQI of 90+: 68
Number of events: 25
  Defined as an episode of heavy smoke with hourly concentrations of 35.5 ug/m^3 at minimum somewhere in Minnesota within a +/-24 hour buffer of an AQI 90+ day, to simulate how we’d handle Air Quality Alerts (continuation vs new alert)
  Each event lasts 2.7 days on average
Notes: *78% of these days were in 2021 and 2023, which has definitely put a damper on our precious warm season as of late. Many Minnesotans have begun routinely checking the air quality forecast like they do the weather forecast.

## Slide 6: PROCESS
Reviewed polar-orbiting satellite hotspot, aerosol optical depth, and visible imagery, geostationary satellite data when available, smoke model forecasts, air quality observations, and Hysplit back-trajectories as needed
Map adapted from NRC
July 6, 2019
Assigned approximate wildfire areas for each event and their approximate smoke path to Minnesota

## Slide 7: Minnesota’s PM2.5 Exceedance-Causing Wildfires 2014-2023
Takeaways:
Apart from a couple events partially in northern WA/ID/MT, no exceedance events from western US wildfires
  An event from 2024 featured mix of Idaho and Saskatchewan smoke
Distances range from near to far
Map adapted from NRC
25 event composite
Notes: *(”Exceedance-Causing” including the 10 AQI buffer (really 90+ AQI))
*Possible explanation is, oftentimes need a cold front. First, low pressure typically develops on the leeward side of the Rockies. Second, cold fronts typically don’t travel from south to north. Storm track climatology: https://www.cpc.ncep.noaa.gov/products/precip/CWlink/MJO/strack.shtml

## Slide 8: Minnesota’s PM2.5 Exceedance-Causing Wildfires 2014-2023
Notes: *The 10 mile wildfire event was partly inside Minnesota as well

## Slide 9: Minnesota Exceedance-Causing Wildfires 2014-2023
Events correspond well to areas of spruce, pine and mixed-wood trees
  Main focus areas when forecasting
Events have originated from wildfires in high and low elevations
Events correspond well to Canada’s National Burned Area Composite from 1972-2023
Takeaways:
Maps adapted from NRC

## Slide 10: Minnesota Exceedance-Causing Wildfires 2014-2023: MAGNITUDE
Max AQI recorded by a Minnesota regulatory monitor color coded by event
Map adapted from NRC
90-100 AQI
101-150 AQI
151-200 AQI
201-300 AQI
Notes: *Note, a few events have more than one oval
*Coincidence that all purple AQI wildfire areas were in a group? Too small of a sample size perhaps to say…

## Slide 11: Minnesota Exceedance-Causing Wildfires 2014-2023: MAGNITUDE
Max one hour concentration recorded by a Minnesota regulatory monitor color coded by event
Map adapted from NRC
35.5-55.4 ug/m^3
55.5-125.4 ug/m^3
125.5-225.4 ug/m^3
225.5+ ug/m^3

## Slide 12: Minnesota Exceedance-Causing Wildfires 2014-2023: DURATION
All events are impactful, some much more than others
Map adapted from NRC
0-1 Days
2 Days
3-6 Days
7+ Days

## Slide 13: Minnesota Exceedance-Causing Wildfires 2014-2023: COVERAGE
Map adapted from NRC
0-1 Monitors
2-9 Monitors
10-19 Monitors
20+ Monitors
All events are impactful, some much more than others

## Slide 14: Minnesota Exceedance-Causing Wildfires 2014-2023: TOTAL
Map adapted from NRC
0-1 Total Exceedances
2-10 Total Exceedances
11-24 Total Exceedances
25-49 Total Exceedances
50+ Total Exceedances
All events are impactful, some much more than others

## Slide 15: Minnesota Exceedance-Causing Wildfires 2014-2023
Map adapted from NRC
Canadian Drought Monitor
All drought classifications within each events’ wildfire areas were included
https://agriculture.canada.ca/en/agricultural-production/weather/canadian-drought-monitor
Notes: *Drought is often cited as a risk for wildfires
*Best guess which involved interpolation on occasion, as Canadian drought maps update once a month as opposed to weekly in the US

## Slide 16: Minnesota Exceedance-Causing Wildfires 2014-2023
Map adapted from NRC
Sometimes difficult to determine since information is updated once a monthly
https://agriculture.canada.ca/en/agricultural-production/weather/canadian-drought-monitor

## Slide 17: Minnesota Exceedance-Causing Wildfires 2014-2023
Map adapted from NRC
Predominant Natural Resource Canada’s Fire Weather Index forecast categories on the day(s) of exceedance-causing wildfire activity
  Like drought, sometimes had multiple categories per event
https://cwfis.cfs.nrcan.gc.ca/maps/fw?type=fwi
Notes: *Used as a general index of fire danger throughout the forested areas of Canada, which takes into account the dryness of fuels, temperature, humidity, level of precipitation and wind speed

## Slide 18: Weather Parameters At Wildfires
3 hourly NCEP North American Regional Reanalysis (NARR) composites
Max values at any time or fraction of the wildfire activity
  Most areas had lower values for most of the “day”
  “Day” extends from 12z to 03z
Notes: *Again, small sample size, but can at least start to glean some information about the wildfire environment
(*) Data distributed into quartiles, and I believe the whiskers extend to 1.5* the Interquartile Range (the box) to set a boundary beyond which would be considered outliers
*https://psl.noaa.gov/cgi-bin/data/narr/plothour.pl

## Slide 19: Mechanisms for Smoke Transport
7am Sept 20th
Map adapted from NRC
Focus on the upper and lower levels of the atmosphere
  500mb height contour(s)
  Surface features
Both on the day of large wildfire smoke output and the approximate hour of heavy smoke intrusion into Minnesota
Since the wildfire location changes from event to event, had to normalize when creating the composite map
7pm June 4

## Slide 20: Mechanisms for Smoke Transport
Composite of 500mb height contour(s) on the day of wildfire growth responsible for heavy smoke intrusion for events who’s wildfires were >350 miles from Minnesota
  <350 mile events often featured heavy wildfire smoke that was produced on the same day/night as it entered Minnesota - wanted to focus on state of atmosphere prior to this time
Map adapted from NRC
Notes: *A couple odd-balls, but by and large, seems to be a common theme involving an upper-level trough in the vicinity or just west of the wildfire location.

## Slide 21: Mechanisms for Smoke Transport
Map adapted from NRC
Composite of surface features on the day of wildfire growth responsible for heavy smoke intrusion for events who’s wildfires were >350 miles from Minnesota
  <350 mile events often featured heavy wildfire smoke that was produced on the same day/night as it entered Minnesota - wanted to focus on state of atmosphere prior to this time
Notes: *A couple odd-balls, but by and large, seems to be a common theme involving a boundary in the vicinity or just west of the wildfire location.

## Slide 22: Mechanisms for Smoke Transport
Map adapted from NRC
Composite of 500mb heights at the time of heavy smoke onset in Minnesota
Notes: *Sometimes the heavy smoke would move in the evening before a 90+ AQI day – wanted to capture the timing of initial onset as close to reality as possible

## Slide 23: Mechanisms for Smoke Transport
Map adapted from NRC
Composite of 500mb heights at the time of heavy smoke onset in Minnesota
Responsible wildfires greater than 350 miles from Minnesota
Responsible wildfires in Quebec or less than 350 miles from Minnesota
Both
Takeaway: The presence of upper-level troughs is a very common theme
Notes: *Try to tease out some additional information - for the most part for wildfires >350 miles away, the upper level trough was to the north or west of Minnesota.

## Slide 24: Mechanisms for Smoke Transport
Map adapted from NRC
Composite of relevant surface features present at the time of heavy smoke onset in Minnesota
Notes: *Bit of a mess, but have a combination of subsidence from high pressure or cold air advection, perhaps pooling of particulates along a boundary other than a cold front such as a surface trough or stationary front, and then ”other”, which includes no apparent feature and/or uncertain features. One event featured smoke that seemed to be brought down from aloft via Lake Michigan, which then transported northwesterly around an area of high pressure. Similar event with Lake Superior influence in 2024. There was also a thunderstorm that influenced heavy ground-level smoke transport in 2021.

## Slide 25: Mechanisms for Smoke Transport
Map adapted from NRC
Composite of relevant surface features present at the time of heavy smoke onset in Minnesota, but only with events who’s wildfires are >350 miles away from MN
Notes: *Cold front is necessary most of the time to get heavy ground-level wildfire smoke when fires are more distant
(*) The map of mechanisms shows surface fronts… position of 850mb front could account for displacements.

## Slide 26: Mechanisms for Smoke Transport
Takeaway: Mechanisms for heavy smoke transport appear less limited when fires are closer
Map adapted from NRC
Same, but only <350 miles and Quebec events
Notes: *Cold fronts still the most common feature, but much closer to being as common as other features
*Does this suggest that the probability for a bad smoke season in Minnesota increases if the potential for Canadian wildfires/drought is greatest closer to home? *While the 2024 Canadian wildfire season started early and was very active throughout, MN only had one exceedance event from May through early August when activity was focused mainly across northeastern British Columbia, but then several additional from mid Aug through mid Sept when numerous large wildfires were active in central Saskatchewan (about twice as close).

## Slide 27: Magnitude of Cold air advection for cold fronts events
Storm Prediction Center’s Hourly Mesoscale Analysis data
Recorded the highest range of CAA associated with a front that led to heavy smoke in Minnesota around the time of the intrusion
Notes: *https://www.spc.noaa.gov/exper/ma_archive/

## Slide 28: Potential Future Work
Continue adding to the dataset
  2024, future years’ events
  Rolling 24 hour average
  Sub-90 AQI events with very high 6-12 hour concentrations
Additional analysis
  Hot Dry Windy Index
    Uses wind speed and vapor pressure deficit in the lower atmosphere
  Satellite-observed Fire Radiative Power
    Relationship between distance from Minnesota and magnitude of FRP necessary for exceedance event?
Do smoke models handle certain ground-level smoke transport mechanisms better than others?
  Timing and concentration
Notes: *Many other ideas
*As for how the NWS AQM guidance could be better/strengths and weaknesses, would be amazing to have a user-defined option for magnitude of FRP - basically allow the user to turn new smoke on and off.
*Example scenario in which models currently struggle summarized by David Brown: "The models don't have the correct emissions for events where the fires grow rapidly in a day. On Friday, May 9th, 2024, the models had Thursday's emissions which were much lower. On Saturday, it was too late because most of the smoke had already been generated and transporting through the atmosphere“